## Slide 1
Wind forecast desk
A day-ahead wind forecasting and error pilot for the trading desk — January 2026
Notes: (~0:00-0:35) Hi, I'm presenting the pilot we ran on day-ahead wind forecasting. You buy power for tomorrow before you know the wind. This tool answers the two questions your desk asked: what forecast did we actually have when we decided, and how wrong is it, in megawatts.

## Slide 2
The problem
You buy electricity for tomorrow, one day ahead.
Wind is free but uncertain, so you forecast it and buy the gap from thermal plants.
The decision is made on D-1, before gate closure (09:20 EPEX, 09:50 N2EX UK time).
So what matters is the forecast that existed when you decided — not the one published after.
Notes: (~0:35-1:15) The desk buys power a day ahead. Wind is free but weather-dependent, so the gap is bought from thermal plants. The decision is made the day before delivery, before the day-ahead auctions close at 09:20 and 09:50 UK time. So the only forecast that counts is the one that existed at decision time.

## Slide 3
Two questions, one rule
1. What was the latest national wind forecast available when we decided?
2. How wrong is that forecast, in MW, so we can size a buffer?
The rule: only forecasts published at or before the decision cutoff count. Everything published later is ignored.
Data: Elexon WINDFOR (forecasts) and FUELHH (actuals), national wind, January 2026.
Notes: (~1:15-1:50) The pilot answers two questions: the latest national wind forecast available at the moment of decision, and how wrong it typically is. One rule makes it fair: only forecasts published at or before the cutoff count. Data is Elexon's national wind only: WINDFOR forecasts and FUELHH actuals.

## Slide 4
January 2026 at a glance
31 decision days
1,488 half-hours checked
2,042 MW
typical miss (mean absolute error)
+1,748 MW
forecast runs high on average — you would be short
5,310 MW
P95 buffer: 19 of 20 half-hours miss by less
Notes: (~1:50-2:30) Over 31 decision days and 1,488 half-hours: the typical miss is about 2 gigawatts. The forecast runs about 1.7 gigawatts high on average — relying on it alone would leave you short. And 19 out of 20 half-hours miss by less than 5.3 gigawatts, which is how you size the buffer.

## Slide 5
Live demo
Decision view · Accuracy view · move the cutoff and watch the numbers change
Notes: (~2:30-5:00) DEMO. Decision view for 5 January, a typical day (MAE 2,093): the 48 half-hours with the forecast that existed at 09:00, the chart with the planning band. Then Accuracy: the metrics, the takeaway, and the horizon chart showing shorter horizons are more accurate. Move the cutoff to 00:00: early slots have no forecast and are dropped and counted. Back to 09:00: nothing dropped. Close with the buffer message.

## Slide 6
What we recommend
Size the buffer from P95: about 5.3 GW covered 19 of 20 January half-hours.
Watch the bias: the forecast runs 1.7 GW high — consider a correction study.
Next: scheduled live ingest, out-of-sample validation, other fuels.
Notes: (~5:00 close) Our recommendation: plan buffers from the P95 miss, and treat the 1.7 gigawatt bias as a known lean while we study a correction. Next steps are a live ingest job, out-of-sample validation, and extending to other fuels. Thank you.